RPM2RT Guide
Author: Kim Miikki
Date:	2.9.2021
# Introduction
This program calculates the revolution time (RT) from a given RPM value. The RT can be used as camera exposure time, flash interval time etc. when capturing images from a rotating system.
# System Requirements
Operating System: ALL
Python 3
# Calculation Method
Inverting the RPM value and then multiplying it with 60 gives the RT value. It is shown in the following equation:
rt={60 s/min} over {revolutions /min}={ 60 }over{ revolutions}s
# Use Cases
Calculate the revolution time when the system is rotating at 2800 RPM:
$ rpm2rt.py 2800
RPM to Revolution Time
Revolution time:
21.43 ms
By adding the optional -b argument, the result is given in bare format (unit of s is hidden):
$ pm2rt.py 2800 -b
0.0214
By using the -a switch (ALL), the RT is presented with these units: s, ms and µs. The output is shown here:
$ rpm2rt.py -a 2800
RPM to Revolution Time
RPM: 2800
=>
Revolution time:
0.0214 s
21.43 ms
21429 µs